## Slide 1: IMPROVED LOCATIONAL ACCURACY OF SCRIM DATA USING GPS
James Mitchell WDM Limited
Philip Blagdon NZTA
Chris Kennedy WDM Limited

## Slide 2: Linear Referencing
Linear referencing divides the highway network into a series of sections.
Length of each section can vary, from 20 -50m at their shortest in Urban areas, up to 15 – 20km at their longest in rural areas.
Start and end of each section is usually defined by start and end nodes.

## Slide 3: Linear Referencing
Survey machines measure the condition along a series of sections.
Fitted with accurate distance measuring devices which typically produce accuracies of ±0.03% or better (±3m per km).
Survey data rubber banded to match section network length.

## Slide 5: Limitations of Linear Referencing
Physical marking of section start and end points will not always remain constant on the road.
Distance measuring systems fitted to survey vehicles contain small and highly controlled inherent errors.
Difficult to follow consistent driveline across multiple surveys.

## Slide 6: Limitations of Linear Referencing
Not an absolute referencing system, but a relative referencing system defining the location of points along the survey that are unique to a given survey pass.
Accuracy will always be balance between cost of maintaining high levels of accuracy and the consequences of accepting lower levels of accuracy.

## Slide 7: Implications for Skid Resistance
Site Categories cannot be ‘fixed’ or defined and maintained separately from a survey.
Accurate trends in skid resistance cannot be established by plotting survey results year on year.

## Slide 8: GPS Referencing
Differential GPS, has improved the accuracy with which survey vehicles travelling at up to 100km/hr can record their location.
During surveys, GPS is received at 100Hz, or at 80km/hr every 0.22m.
Accuracy of 10m boundaries of elapsed distance can be defined to co-ordinate accuracies of about ±1m.

## Slide 9: DSB Referencing
GPS co-ordinates used to accurately define section start and end points.
Recorded section length stretched or shrunk to equal network length.
Co-ordinates for each 10m boundary stored as the 10m co-ordinates for future surveys, baseline co-ordinates.

## Slide 10
10m
10m
10m
10m
10m

## Slide 11: DSB Referencing
For subsequent surveys, data subdivided into 10m lengths by the baseline co-ordinates.
Single carriageway roads, same baseline used for 2 directions so that data aligns across the carriageway.
Co-ordinates taken at the start of 10m section for increasing direction and end of 10m section for decreasing direction.

## Slide 12: DSB Co-ordinates
NZTA NMA | Year 2 2008/09 > 2.5m | Year 3 2009/10 > 2.5m | Survey Length/km
Napier | 4.5% | 1.8% | 370.15
Gisborne | 3.9% | 2.2% | 153.64
Central Waikato | 3.7% | 4.1% | 451.44
West Wanganui | 2.6% | 2.0% | 546.58
Rotorua | 3.1% | 2.7% | 164.56
South Canterbury | 1.6% | 0.9% | 542.92
Central Otago | 2.4% | 0.5% | 503.31
Overall | 2.9% | 1.9% | 2732.60

## Slide 13: SH 53 Linear Referencing

## Slide 14: SH 53 DSB Referencing

## Slide 15: SH 53 Linear Referencing

## Slide 16: SH 53 DSB Referencing

## Slide 17: Alignment across Carriageway Linear Referencing

## Slide 18: Alignment across Carriageway DSB Referencing

## Slide 19: DSB Referencing
With linear referencing condition measurements can have an offset of 30 - 40m between surveys. This no longer occurs with DSB referencing.
Able to compare lanes across the carriageway.

## Slide 20: Limitations
GPS signal not available for long periods.
Single carriageway sections do not have same vehicle track for 2 directions.
Road alignment changes between surveys.